PART 1	GENERAL

1.1	SUMMARY

- Provide all equipment and materials, and do all work necessary to furnish and install the Soccer Equipment, as indicated on the drawings and as specified herein.

1.2	RELATED WORK

- Examine Contract Documents for requirements that affect work of this section.  Other specification sections that directly relate to work of this Section include, but are not limited to:

  - Section 02200 - Earthwork; Excavation and Backfill and establishment of subgrade elevations.

  - Section 02511 - Asphalt Concrete Pavement

  - Section 02535 - Synthetic Track Surfacing

  - Section 02542 - Synthetic Field Surfacing

  - Section 03300 - Cast-in-Place Concrete; Concrete foundations and bases for goals.

1.3		REFERENCES

- Comply with applicable requirements of the following standards.  Where these standards conflict with other specified requirements, the most restrictive requirements shall govern.

      - U.S. Tennis Court and Track Builders Association

      - National Federation of State High School Associations (NFSHSA)

      - National Collegiate Athletic Association (NCAA)

      - International Amateur Athletic Foundation (I.A.A.F.)

      - Manufacturers Data and Recommended Installation Requirements.

1.4		SUBMITTALS

- Manufacturers Product Data

            - Provide manufacturer’s product literature, technical specifications and other data prior to actual field installation work for Architect or Owner’s Representative review.

# Shop Drawings

  - Provide drawings of manufacturers recommended installation and foundation requirements prior to actual field installation work for Architect or Owner’s Representative review.

1.5		QUALITY ASSURANCE

- Manufacturers warranties shall pass to the Owner and certification made that the product materials meet all applicable grade trademarks or conform to industry standards and inspection requirements.

1.6	DELIVERY, STORAGE AND HANDLING

- Materials delivered to the site shall be examined for concealed damage or defects in shipping. Any defects shall be noted and reported to the Owner’s Representative.

- Replacements, if necessary, shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- Sound materials shall be stored above the ground under protective cover or indoors so as to provide proper protection.

PART 2	PRODUCTS

2.1		MANUFACTURERS

- Manufacturers and product selections named are provided to establish the minimum standard.

      - Soccer Equipment - As manufactured by AAE (Aluminum Athletic Equipment Co.); 1000 Enterprise Drive, Royersford, PA 19468; Toll Free (800) 523-5471.

2.2		Soccer EQUIPMENT

- Portable Soccer Goals - Shall be as manufactured by AAE:

  - Model # SGR-P (portable), Crossbar 4" round one-piece custom slotted  x 1/8" wall x 24'-8" lg. 6061T6 custom aluminum extrusion tube w/ 2 welded stay sockets powder-coated white, Uprights 4" round custom slotted x 1/8" wall x 92" long 6061T6 custom aluminum extrusion w/ 1 welded stay socket powder-coated white, Uprights attach to crossbar via 3-3/4" round x 8" long solid heavy-duty UHMW connectors, Stay 2" square custom slotted x .125" wall 6063T4 aluminum tube 21'-2" lg. x 3' top x 8' bottom, Groundbar 2" square custom slotted x 24'-0" lg. 6061T6 alum. tube w/ endplates, molded net clips for net attachment, stainless steel and galvanized hardware, includes anchor hardware

Additional Models/Sizes:

SGR-P/12 (round – 6'-6"x 12'-0")

SGR-P/18.5 (round – 6'-6"x 18'-6")

SGR-P/21 (round – 7'-0"x 21'-0")

  - Model # SGR-SP (semi-permanent), Crossbar 4" round one-piece custom slotted  x 1/8" wall x 24'-8" lg. 6061T6 custom aluminum extrusion tube w/ 2 welded stay sockets powder-coated white, Uprights 4" round custom slotted x 1/8" wall x 116" long 6061T6 custom aluminum extrusion w/ 1 welded stay socket and 1 welded open receptacle hinge device powder-coated white,  Uprights attach to crossbar via 3-3/4" round x 8" long solid heavy-duty UHMW connectors, Loop Stay 1.25" round x .125" wall x 3' deep 6063T4 aluminum tube, Groundbar 2" square custom slotted x 24'-0" lg. 6061T6 aluminum w/ welded corner receptacles and hinge mechanism for storing groundbar against goal face when mowing or doing maintenance to field, molded net clips for net attachment, stainless steel and galvanized hardware, includes four (4) aluminum ground sleeves for contractor installation

Additional Models/Sizes:

SGR-SP/12 (round – 6'-6"x 12'-0")

SGR-SP/18.5 (round – 6'-6"x 18'-6")

SGR-SP/21 (round – 7'-0"x 21'-0")

  - Model # SGR-P/I (portable EUROPA), Crossbar 4" round one-piece custom slotted  x 1/8" wall x 24'-8" lg. 6061T6 custom aluminum extrusion tube w/ 2 welded stay sockets powder-coated white, One-piece “L” Uprights 4" round custom slotted x 1/8" wall x 92" high x 84" deep 6061T6 custom aluminum extrusion w/ 1 welded stay socket powder-coated white, Uprights attach to crossbar via 3-3/4" round x 8" long solid heavy-duty UHMW connectors, Loop Stay 1.25" round x .125" wall x 3' deep 6063T4 aluminum tube, Groundbar 4" round custom slotted x 24'-8" lg. 6061T6 aluminum tube, molded net clips for net attachment, stainless steel and galvanized hardware, includes anchor hardware

Additional Models/Sizes:

SGR-P/I/12 (round – 6'-6"x 12'-0")

SGR-P/I/18.5 (round – 6'-6"x 18'-6")

SGR-P/I/21 (round – 7'-0"x 21'-0")

  - Model # SGR-SP/I (semi-permanent EUROPA), Crossbar 4" round one-piece custom slotted  x 1/8" wall x 24'-8" lg. 6061T6 custom aluminum extrusion tube w/ 2 welded stay sockets powder-coated white, Uprights 4" round custom slotted x 1/8" wall x 116" high 6061T6 custom aluminum extrusion w/ 1 welded stay socket and 1 welded open channel groundbar receptacle powder-coated white, Uprights attach to crossbar via 3-3/4" round x 8" long solid heavy-duty UHMW connectors, Loop Stay 1.25" round x .125" wall x 3' deep 6063T4 aluminum tube, Groundbar 2" square custom slotted x 24'-0" lg. 6061T6 aluminum w/ welded corner receptacles and hinge mechanism for storing groundbar against goal face when mowing or doing maintenance to field, molded net clips for net attachment, stainless steel and galvanized hardware, includes four (4) aluminum ground sleeves for contractor installation

Additional Models/Sizes:

SGR-SP/I/12 (round – 6'-6"x 12'-0")

SGR-SP/I/18.5 (round – 6'-6"x 18'-6")

SGR-SP/I/21 (round – 7'-0"x 21'-0")

  - Model # TSG (Training Soccer Goal), Crossbar 4" round one-piece custom slotted  x 1/8" wall x 24'-8" lg. 6061T6 custom aluminum extrusion tube powder-coated white, One-piece “L” Uprights 4" round custom slotted x 1/8" wall x 44" high x 44" deep 6061T6 custom aluminum extrusion powder-coated white, Uprights attach to crossbar via 3-3/4" round x 8" long solid heavy-duty UHMW connectors, Groundbar 4" round custom slotted x 24'-8" lg. 6061T6 aluminum tube, molded net clips for net attachment, stainless steel and galvanized hardware, includes anchor hardware

  - Model # SN-3/24-W (Soccer Net), High Visibility White 3 mm twine polyethylene braided 5” square mesh net, measures 24’ wide by 8’ high by 4’ top depth and 10’ bottom depth with a 1/4” MFP rope border Also available in Orange(-O), Red(-R) & Yellow(-Y)

  - Model # SN-4/24-W (Soccer Net), High Visibility White 4 mm twine polyethylene braided 5" square mesh net, measures 24' wide by 8' high by 4' top depth and 10' bottom depth with a 1/4" MFP rope border

Also available in Orange(-O), Blue(-B), Yellow(-Y) & Red(-R)

  - Model # SN-6/24-O (Soccer Net), High Visibility Orange 6 mm twine polyethylene braided 5” square mesh net, measures 24’ wide by 8’ high by 4’ top depth and 10’ bottom depth with a 1/4” MFP rope border

  - Model # SN-CLUB (Soccer Net), High Visibility White 3 mm twine polyethylene braided 5” square mesh net, measures 6’-6” wide by 12’ high by 2’ top depth and 7’ bottom depth with a 1/4” MFP rope border

Additional Sizes:

SN-CLUB (6’-6” wide by 18’-6” high by 2’ top depth & 7’ bottom depth)

SN-CLUB (7’ wide by 21’ high by 3’ top depth & 7’-6” bottom depth)

  - Model # SGW-40, 16”L x 9”W x 1”H HRS Steel Plate with welded 3” x 3/8” thick C-channel, handle slot cut into plate, vinyl coated “Caution Yellow”, weighs 40 lbs.

  - Model # VSZ-Y, 18”L x 18”W yellow vinyl sandbag with sewn in zipper and canvas handles, holds 60 lbs. weight.

  - Model # VSB, Vinyl Saddle Bag, 14”W x 30” L Vinyl bag with 2” wide sewn in handle centered with rubberized grip, Velcro flap sewn in one end for adding sand, weighs 50 lbs.

  - Model # RW-SG, removable 10” pneumatic tires mounted on a 3/4” dia. stainless steel axle.

  - Model # RW-SG-I, 10” pneumatic tires mounted on 3/4” dia. stainless steel axle, RW-SG-F included to adapt to 2” sq. large loop stay on SGR-P, flip to engage.

PART 3	EXECUTION

3.1  		INSPECTION

- Examine the areas and conditions where equipment and systems are to be installed and notify the contractor of conditions detrimental to the proper and timely installation and completion of the work.

- Do not proceed with the work until unsatisfactory conditions have been corrected by the contractor in a manner acceptable and to the satisfaction of the Architect/Engineer or Owner's Representative.

3.2	INSTALLATION

- All athletic equipment shall be installed as indicated on approved submittals as recommended and in strict accordance with manufacturer's written directions and as indicated on the drawings and specified herein.

- All concrete footings for athletic equipment shall be installed as indicated on the drawings and in accordance with Section 03300, Cast-in-Place Concrete.

- All sleeves required for athletic equipment installation shall be set plumb and true to line and grade in concrete as indicated on the drawings and per manufacturer's recommendation.

- All athletic equipment shall be installed in strict accordance with the latest rules, regulations and specifications governing that sport or event for which it is being installed.

3.3  		TESTING, ADJUSTMENT AND OPERATION

- All athletic equipment requiring testing, adjustments and operation shall be tested for proper operation and adjusted to conform to specified standards.

- Provide certifications as required, indicating that equipment has been tested and adjusted to conform to specified standards.

- Provide operating and maintenance instructions and manuals to Owner -designated personnel for the proper operation and care of equipment after equipment has been tested and adjusted to conform to specified standards.

3.4  		CLEANING

- Upon completion of work in any given area, remove all trash and debris from the work area and leave in clean condition.

- END OF SECTION -