PART 1	GENERAL

1.1	SUMMARY

- Provide all equipment and materials, and do all work necessary to furnish and install the High Jump Landing Pad Equipment, as indicated on the drawings and as specified herein.

1.2	RELATED WORK

- Examine Contract Documents for requirements that affect work of this section.  Other specification sections that directly relate to work of this Section include, but are not limited to:

  - Section 02200 - Earthwork; Excavation and Backfill and establishment of subgrade elevations.

  - Section 02511 - Asphalt Concrete Pavement

  - Section 02535 - Synthetic Track Surfacing

  - Section 02542 - Synthetic Field Surfacing

  - Section 03300 - Cast-in-Place Concrete; Concrete foundations and bases for goals.

1.3		REFERENCES

- Comply with applicable requirements of the following standards.  Where these standards conflict with other specified requirements, the most restrictive requirements shall govern.

      - U.S. Tennis Court and Track Builders Association

      - National Federation of State High School Associations (NFSHSA)

      - National Collegiate Athletic Association (NCAA)

      - International Amateur Athletic Foundation (I.A.A.F.)

      - Manufacturers Data and Recommended Installation Requirements.

1.4		SUBMITTALS

- Manufacturers Product Data

            - Provide manufacturer’s product literature, technical specifications and other data prior to actual field installation work for Architect or Owner’s Representative review.

# Shop Drawings

  - Provide drawings of manufacturers recommended installation and foundation requirements prior to actual field installation work for Architect or Owner’s Representative review.

1.5		QUALITY ASSURANCE

- Manufacturers warranties shall pass to the Owner and certification made that the product materials meet all applicable grade trademarks or conform to industry standards and inspection requirements.

1.6	DELIVERY, STORAGE AND HANDLING

- Materials delivered to the site shall be examined for concealed damage or defects in shipping. Any defects shall be noted and reported to the Owner’s Representative.

- Replacements, if necessary, shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- Sound materials shall be stored above the ground under protective cover or indoors so as to provide proper protection.

PART 2	PRODUCTS

2.1		MANUFACTURERS

- Manufacturers and product selections named are provided to establish the minimum standard.

      - High Jump Landing Pad Equipment - As manufactured by AAE (Aluminum Athletic Equipment Co.); 1000 Enterprise Drive, Royersford, PA 19468; Toll Free (800) 523-5471.

2.2		HIGH JUMP LANDING PAD SYSTEMS

- High Jump Landing Pad System- Shall be as manufactured by AAE:

  - Model # SHJ-26, High Jump Landing Pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 26” high x 18’-0” wide x 12’-0” deep;  Base Units include foam types 21120 (21# - 1.2 density), 33120 (33# - 1.2 density), 40130 (40# - 1.3 density); system includes three (3) Base Unit Foam Assemblies: three (3) base units each 26” x 6’-0” x 12’, all units are comprised of a four (4) layer cross pattern foam assembly construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked heavy duty nylon web strap w/ military-spec snap hooks for easy attachment;  PLEASE NOTE: Warning Labels on all units

  - Model # SWC-26, Weather Cover, one (1) Weather Cover 22oz. double knife-coated vinyl (standard color gray, custom colors available), box-tacked heavy duty nylon web strap w/ military-spec snap hooks for easy attachment to be used w/ Model # SHJ-26

  - Model # SHJ-28, High Jump Landing Pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 28” high x 18’-0” wide x 12’-0” deep;  Base Units include foam types 21120 (21# - 1.2 density), 33120 (33# - 1.2 density), 40130 (40# - 1.3 density); system includes three (3) Base Unit Foam Assemblies: three (3) base units each 26” x 6’-0” x 12’, all units are comprised of a four (4) layer cross pattern foam assembly construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Top Pad to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ additional 2” thick solid foam pad and skirted 18oz. double knife-coated vinyl sides (color as specified) top pad includes heavy duty zipper surround for foam insertion, box-tacked strap w/ military-spec snap hooks for easy attachment;  PLEASE NOTE: Warning Labels on all units

  - Model # SWC-28, Weather Cover, one (1) Weather Cover 22oz. double knife-coated vinyl (standard color gray, custom colors available), box-tacked heavy duty nylon web strap w/ military-spec snap hooks for easy attachment to be used w/ Model # SHJ-28

  - Model # HJBP, High Jump Base Pad, one (1) Base Pad 22oz. double knife-coated vinyl (color as specified), sewn 22oz. double knife-coated vinyl flap w/ military-spec Velcro, serves as protective padding around AAE Standard Model #s MJS & RJS High Jump Standards, to be used in conjunction with all high jump pad systems

PART 3	EXECUTION

3.1  		INSPECTION

- Examine the areas and conditions where equipment and systems are to be installed and notify the contractor of conditions detrimental to the proper and timely installation and completion of the work.

- Do not proceed with the work until unsatisfactory conditions have been corrected by the contractor in a manner acceptable and to the satisfaction of the Architect/Engineer or Owner's Representative.

3.2	INSTALLATION

- All athletic equipment shall be installed as indicated on approved submittals as recommended and in strict accordance with manufacturer's written directions and as indicated on the drawings and specified herein.

- All concrete footings for athletic equipment shall be installed as indicated on the drawings and in accordance with Section 03300, Cast-in-Place Concrete.

- All sleeves required for athletic equipment installation shall be set plumb and true to line and grade in concrete as indicated on the drawings and per manufacturer's recommendation.

- All athletic equipment shall be installed in strict accordance with the latest rules, regulations and specifications governing that sport or event for which it is being installed.

3.3  		TESTING, ADJUSTMENT AND OPERATION

- All athletic equipment requiring testing, adjustments and operation shall be tested for proper operation and adjusted to conform to specified standards.

- Provide certifications as required, indicating that equipment has been tested and adjusted to conform to specified standards.

- Provide operating and maintenance instructions and manuals to Owner -designated personnel for the proper operation and care of equipment after equipment has been tested and adjusted to conform to specified standards.

3.4  		CLEANING

- Upon completion of work in any given area, remove all trash and debris from the work area and leave in clean condition.

- END OF SECTION -